Generating Thresholds, Landmark and Waypoint Data
For each waypoint, Pre-flight image and some navigation data will be required to generate image processing thresholds, landmark data and waypoint data.

Requirements:
From the flight data following parameters shall be collected.
1. Waypoint image: with minimum of THREE visual landmarks. Ideally FOUR landmarks are preferred.
2. Altitude (in meters): Altitude can be obtained by looking at navigation data when image was captured.
3. Yaw angle (in degrees): Yaw angle can also be obtained by looking at navigation data when image was cpatured.

Pre-Processing:
Following process shall be completed for each waypoint image.
Rename Source Image and Generate Sub-images
All source image and sub-images should be placed in folder Database inside work folder.
If there are FOUR landmarks in the image, assuming landmarks are marked as 0, 1, 2 , 3 (Note: Python indexing starts from 0. Numbers were chosen in accordance with Python indexing convention)
Landmark that has highest centroid y-value in the image plane (i.e. the landmark on the bottom most position ) is indexed with 0 and indexing is increased as centroid y-value increases.
It should be named with following naming convention:
waypoint_waypoint_number_parLmrkNos.jpg
where
waypoint_number = waypoint number in navigation sequence
parLdmrkNos = different landmark combination sets with THREE landmarks out of	FOUR landmarks
parLdmrkNos field shall be set to 0 while generating data with all FOUR landmarks.
parLdmrkNos field shall be set to 012, 013, 023, 123 for landmark combinations different landmark combinations.

Example: for waypoint_number = 1:
Waypoint image with all four landmarks shall be named as waypoint_1_0.jpg
Waypoint image with landmarks 0, 1 and 2 shall be named as waypoint_1_012.jpg
Waypoint image with landmarks 0, 1 and 3 shall be named as waypoint_1_013.jpg
Waypoint image with landmarks 0, 2 and 3 shall be named as waypoint_1_023.jpg
Waypoint image with landmarks 1, 2 and 3 shall be named as waypoint_1_123.jpg

Four image files with partial landmarks (parLdmrkNos != 0) shall be edited to remove one landmark that doesnot appear in parLdmrkNos field. For example, for waypoint_1_012.jpg, landamrk 3 should be removed from image file. This can be done by using simple image editor such as Paint (in Windows) or Pinta (in Ubuntu). For this, nearby background should be cropped and covered the landmark.

Remainder of pre-processing shall be completed by changing parameters in Python file “ImProTest.py", in the main repository.
Threshold ajustments:
Case 1: Waypoint with FOUR landmarks
Test Images
When the waypoint image has four landmarks:
In file ImProTest.py (Refer to Python file for more description of these parameters):
Following thresholds shall be fixed :
NLdmrk = [4]
Follwoing parameters shall be adjusted as per requirment (In first instance, try with default values):
1. ImageTh: deafult value = 0.004
2. BinaryTh: deafult = 110
3. BinaryThIncDec: deafult = 5
4. BwAreaTh: deafult = [200,2000]
5. LdmrkAngTh: deafult = 5
6. ImCropTh: deafult = [100,36]
7. WpAngTh: deafult = 5
8. WpSiRatTh: deafult = 0.1
Following parameters should be copied from navigation data:
1. AltRef: Altitude of UAV when reference image was captured.
2. YawRef: Yaw angle of UAV when reference image was captured.

Generating Data:
Following parameters in ImProTest.py file shall be set for generating data:
1. GenData = True
2. parLdmrakNos = ‘0’
Run ImProTest.py file and observe if program runs successfully and produces following two lines of output at the end:
Data Successfully written to Database
IpCalDrift = [0.0, 0.0]
A numpy file with following naming convention will be saved in Database sub-folder in main repository:
Wp_waypoint_number_Data.npy
where
waypoint_number = waypoint number in navigation sequence
This process will generate data with all FOUR landamrks in the image.

Once the data is genarated with all FOUR landamrks, data shall be generated for four different cases of partial landmarks (parLdmrkNos = ‘012’ , ‘013’, ‘023’ and ‘123’).
As all data for all cases will be saved in same data file, data for all FOUR landmarks should alwaybes be genrated first. This initializes fields for saving data for partial landmarks. Next, data for partial landmarks should be generated. Data for FOUR landmarks should not be genarated generated again as this will reset data for partial landmark cases. It is recommended to change value of parLdmrkNos one at a time.

Once these steps are completed data will be saved in the folling location: main-repo/Database.

Navigation with Image Processing
Once landmark and waypoint data are saved in correct location, navigation can be perfomred such that the UAV navigates over visual waypoints. Python navigation code can be run under under three different scenarios:
1. Simulation
2. Hardware in the Loop (HiL)
3. Flight Test
VisNav.py Python file in the main repository shall be used to perform all navigation tasks. All three cases can be attanined by changing parameters in VisNav.py file. Brief description of these parameters can be found in the Python file itself.
In following subsections, different navigation scenarios will be described in futher detail.

Simulation
Parameter Setting
Refer to VisNav.py Python file for these parameters.
1. totTrials = 1	This means ONE experiment is conducted in per program run.
2. useRPi = False	This means Raspberry Pi is not used during experiments (i.e. program	is executed in Simulation mode)
3. HiL = False	This parameter has no effect in when useRPi flag is set to False.
4. ImgPro = False	When set to False, drift calculated by image processing will not be	used. In open loop simulation drift can not be calculated.
5. AutoWpTh = 10	This is set to 10 for Simulation experiment. This parameter is useful	while conducting HiL or Flight Test experiments in collecting images	from pre-flight tests.
6. RollCdMax = 0	Not used in Simulation.
7. TiOutTh = 2	Not used in Simulation.
8. AutoWps = [ ]	Not used in Simulation. Set to empty matrix ([ ])
9. VisualWpsSim =	2D matrix containting XY co-ordinate position of visual waypoints example:	used in simulation. These waypoint coordinates are relative to starting [[0,50],[50,50],[50,0]]	point of simulation. Starting point of simulation is always [0,0]
10. VisualWps = []	Not used in Simulation. For HiL and Flight Tests GPS coordinates	(latitude,longitude) of visualwaypoint upto 7 decimal places
Test Image
Once parameter are set, for each landmark one test image will be requried. For the purpose of simulation, images already used to generate landmark and waypoint data could be used. However, they should be named with following naming convention:
waypoint_waypoint_number_test.jpg
where,
waypoint_number = waypoint number in navigation sequence
These files should then be placed in follwing directory: main-repo/FlightData/Simulation.

Running the Program
Simulation is performed by running VisNav.py Python file.
In HiL and fight tests, after initial launch, the UAV is flown in Auto mode before switching to fly by wire mode for autonomous vision-based navigation. In case of simulation, there is no such switching is possible to simulate. Hence in the simulation mode, program is wait to make user input as keyboard ‘Enter’. This action is similar to the switching performed in HiL and flight tests. Postion of the UAV is set to [0, 0] in XY co-ordinate when Enter button is pressed in the keyboard and other visual waypoints co-ordinates are relative to this.
Output
The console show up a number of messages including
Following output will show up in the final line of the console if everything goes wright with the program:
Navigation has been successfully successfully accomplished. Data log files have been saved.
In case there are problems in image processing section following error message will be displayed in the final line of the console:
IMAGE PROCESSING ERROR: Navigation has been aborted.
In case if there are problems in some other places in the code following error message will be displayed in the console.
NAVIGATION INCOMPLETE ERROR: Did not pass through all wps.