Generating Thresholds, Landmark and Waypoint Data
For each waypoint, Pre-flight image and some navigation data will be required to generate image processing thresholds, landmark data and waypoint data.

Requirements:
From the flight data following parameters shall be collected.
1. Waypoint image: with minimum of THREE visual landmarks. Ideally FOUR landmarks are preferred.
2. Altitude (in meters): Altitude can be obtained by looking at navigation data when image was captured.
3. Yaw angle (in degrees): Yaw angle can also be obtained by looking at navigation data when image was cpatured.

Pre-Processing:
Following process shall be completed for each waypoint image.
Rename Source Image and Generate Sub-images
All source image and sub-images should be placed in folder Database inside work folder.
If there are FOUR landmarks in the image, assuming landmarks are marked as 0, 1, 2 , 3 (Note: Python indexing starts from 0. Numbers were chosen in accordance with Python indexing convention)
Landmark that has highest centroid y-value in the image plane (i.e. the landmark on the bottom most position ) is indexed with 0 and indexing is increased as centroid y-value increases.
It should be named with following naming convention:
waypoint_waypoint_number_parLmrkNos.jpg
where
waypoint_number = waypoint number in navigation sequence
parLdmrkNos = different landmark combination sets with THREE landmarks out of	FOUR landmarks
parLdmrkNos field shall be set to 0 while generating data with all FOUR landmarks.
parLdmrkNos field shall be set to 012, 013, 023, 123 for landmark combinations different landmark combinations.

Example: for waypoint_number = 1:
Waypoint image with all four landmarks shall be named as waypoint_1_0.jpg
Waypoint image with landmarks 0, 1 and 2 shall be named as waypoint_1_012.jpg
Waypoint image with landmarks 0, 1 and 3 shall be named as waypoint_1_013.jpg
Waypoint image with landmarks 0, 2 and 3 shall be named as waypoint_1_023.jpg
Waypoint image with landmarks 1, 2 and 3 shall be named as waypoint_1_123.jpg

Four image files with partial landmarks (parLdmrkNos != 0) shall be edited to remove one landmark that doesnot appear in parLdmrkNos field. For example, for waypoint_1_012.jpg, landamrk 3 should be removed from image file. This can be done by using simple image editor such as Paint (in Windows) or Pinta (in Ubuntu). For this, nearby background should be cropped and covered the landmark.

Remainder of pre-processing shall be completed by changing parameters in Python file “ImProTest.py", in the main repository.
Threshold ajustments:
Case 1: Waypoint with FOUR landmarks
Test Images
When the waypoint image has four landmarks:
In file ImProTest.py (Refer to Python file for more description of these parameters):
Following thresholds shall be fixed :
NLdmrk = [4]
Follwoing parameters shall be adjusted as per requirment (In first instance, try with default values):
1. ImageTh: deafult value = 0.004
2. BinaryTh: deafult = 110
3. BinaryThIncDec: deafult = 5
4. BwAreaTh: deafult = [200,2000]
5. LdmrkAngTh: deafult = 5
6. ImCropTh: deafult = [100,36]
7. WpAngTh: deafult = 5
8. WpSiRatTh: deafult = 0.1
Following parameters should be copied from navigation data:
1. AltRef: Altitude of UAV when reference image was captured.
2. YawRef: Yaw angle of UAV when reference image was captured.

Generating Data:
Following parameters in ImProTest.py file shall be set for generating data:
1. GenData = True
2. parLdmrakNos = ‘0’
Run ImProTest.py file and observe if program runs successfully and produces following two lines of output at the end:
Data Successfully written to Database
IpCalDrift = [0.0, 0.0]
This process will generate data with all FOUR landamrks in the image.

Once the data is genarated with all FOUR landamrks, data shall be generated for four different cases of partial landmarks (ParLdmrkNos = ‘012’ , ‘013’, ‘023’ and ‘123’)